## Slide 1: LAB and Simulation - Vehicle and Traffic Safety
Adipta Laha -- Fikri Farhan Witjaksono -- Jan-Hendrik Duerkop

## Slide 2: Task and Test Plan
What is the maximum car weight the existing design can support without encountering problems that the “car” front structure bottoms out?
Test | Distance [cm] | Added Mass [kg] | Velocity [m/s] | Length (post) [cm]
1 | X | 6 | 2.94 | 7.4
2 | X-30 | 4 | 2.7 | -
3 | X-20 | 4 | 2.81 | -
4 | X-5 | 4 | 2.9 | -
5 | X-5 | 4 | 2.9 | 7.6
6 | X-10 | 2 | 2.94 | -
7 | X-10 | 2 | 2.94 | 8

## Slide 3: Deformation vs Time and Added Mass
Chose the 2mm mesh, because of the compromise between simulation accuracy and computation time (cost)
Chart: Deformation vs Added Mass
| 6 | 4 | 2
Experimental | 66 | 64 | 60
Simulation | 66.3 | 62.9 | 58.9
Chart: Deformation vs Time in Simulation
| 0 | 5 | 10 | 15 | 20 | 25 | 30 | 35 | 40 | 45 | 50 | 55 | 60
Test 3 Simulation | 0 | 10.2 | 22.4 | 32.9 | 41.7 | 48.5 | 53.5 | 56.9 | 58.7 | 58.9 | 58.2 | 58.2 | 58.2
Test 2 Simulation | 0 | 10.3 | 22.6 | 33.3 | 42.5 | 49.6 | 55.2 | 59.3 | 61.9 | 62.9 | 62.4 | 62.1 | 62.1
Test 1 Simulation | 0 | 10.3 | 22.7 | 33.7 | 43.2 | 50.8 | 57.1 | 61.9 | 65.1 | 66.3 | 65.7 | 65.6 | 65.6
Bottoming Out Simulation | 0 | 10.6 | 23.9 | 36.2 | 48.7 | 60 | 70.7 | 80.7 | 90.2 | 99 | 107 | 114 | 120

## Slide 4: Validation of data
Validation of the can thickness is done by comparing the above graphs.

## Slide 5: Result
Keep adding mass in the simulation
   higher deformation
Simulation | Test | Added Mass (kg) | Deformation [mm]
 | 1 | 6 | 66.3
 | 2 | 4 | 62.9
 | 3 | 2 | 58.9
Bottomed Out (85% Deformation) | - | 50,1 | 120